DAVID LAZENBY& COMPANY LTD

UNIT 2A, BANTEL WORKS, RYE ROAD, HODDESDON, HERTS ENGLAND

TELEPHONE H0DDESDON 63637 (SALES)

DAVID LAZENBY		Works:	Unit 2A
				Bantel Works
AND COMPANY LTD.			Rye Road
				Hoddesdon
Directors:	D.R. Lazenby			Herts.
         	A.C. Sorensen
	H.W. Weisselberg (USA)			Hoddesdon 63636/7

HAWKE DL6A/B		FORMULA “ATLANTIC”/B

CHASSIS:	Multi—tubular construction of 16, 18 and 20 SWG tube and incorporating stressed outriggers to carry bag tanks.

BODY: Lightweight colour impregnated fibre glass and consisting of detachable nose piece, separate side panels, top panel and rear engine cover. The cockpit is fully upholstered and seating fully adjustable.

SUSPENSION: Ultra—wide based top front wishbone and wide based bottom front wishbone, radius arm and parallel link rear suspension, adjustable anti-roll bars front and rear. Dampers are “SPAX” with adjustable ratings and spring platform heights. All pivots are “Wafe Alinabal” self— aligning ball joints or rod ends which require no lubrication. All suspension parts are chromed.

WHEELS:  ‘L’ 122 magnesium alloy, front 10 x 13”, rear 14 x 13”.

BRAKES:  AR calipers, FR/rear with 10" front and 10” rear discs. Balance bar adjustment of ratios between front and rear.

STEERING: This is by a special high ratio rack and pinion. Bumpsteer easily eliminated by means of a simple vernier adjustment on rack. 10” diameter leather steering wheel. Column adjustable for reach.

FUEL SYSTEM:  Capacity 16 imperial gallons contained in two 8 gallon foam filled bag tanks. Flush fitting single filler cap on both tanks. Safety valve fitted on breather pipe. Tanks separated from cockpit by aluminium sheeting, thus providing a “liquid free” cockpit.

COOLING:	Fully ducted copper and brass water radiator mounted low down at the front. Aluminium oil cooler mounted at the rear.

INSTRUMENTS:	Smith’s 3” diameter chronometric tachometer. Water temperature, oil temperature and oil pressure gauges. Fuel pressure optional.

ELECTRICS:	12 volt aircraft type Varely battery.  Individual switches for ignition, starter and fuel pump.

GEARBOX:	Hewland FT 200 5-speed and reverse.  Gear lever fully adjustable for position.

DRIVE SHAFTS:	(Intermediate) 03 series U/J's/metalastic couplings.

STANDARD EQUIPMENT:	Full harness seat belts, Automatic fire extinguishing system. Tyres to choice.

Hawke DL2B Formula Ford

Page 2

SPECIFICATIONS

CHASSIS:	Multi-tubular nickel bronze welded construction utilizing 16, 18 and 20 SWG tube providing maximum cockpit area protection and high torsional strength.

BODY:	Ultra light-weight color impregnated fiberglass body designed to facilitate access to all mechanical components.

SUSPENSION:	Ultra wide-based wishbone and trailing link front suspension; radius arm and parallel link rear suspension, with adjustable camber, castor and toe-in front and rear.

BRAKES:	Girling hydraulic with 9 1/2” and 10” discs. Balance bar adjustment of ratios between front and rear brakes.

SHOCK

ABSORBERS:	Armstrong or Spax. Adjustable ratings and spring platforms front and rear.

ENGINE:	1,600cc Crossflow engine modified to within the maximum limits of the regulations set by the Formula Ford register, run in and dyno tested.

TRANSMISSION:	Hewland M1( 8 four-speed and reverse gearbox with 9:31 C.W.P. and gear ratios to choice. Gear lever position fully adjustable.

COOLING:	Front mounted cross-f low oil/water radiator with adequate cooling for tropical climates.

WHEELS:	5 l/2J x 13” pressed steel wheels front and rear. Fitted with latest racing tires.

INSTRUMENTS:	Chronometric tachometer, oil pressure and water temperature gauges.

FUEL SYSTEM:	Aluminium seat tank, capacity 8 imp. gallons.

STEERING:	High geared lightweight rack and pinion. 10” leather-covered steering wheel and adjustable center-mounted column.

ELECTRICAL

SYSTEM:	Lightweight Varley dry battery.

COLORS:		Red, Green, White, Blue, Orange, Yellow.